## Slide 1: FPGAs

## Slide 2: Field Programmable Gate Array
Contain an array of programmable logic blocks
Includes simple Boolean logic blocks (OR AND etc)
Also may include memory elements (Flip-Flops or more complete blocks of memory)
Notes: An FPGA is an IC that can be reprogrammed after manufacture

## Slide 4: What is an FPGA used for?
Can be used to solve any problem which is computable
Many applications including:
  Aerospace
  Data centres
  Communications
  Security
Notes: Can implement a soft processor
Aerospace
Avionics, Missiles and Munitions
Data centres
Servers, Routers
Communications
Network processing, baseband
Security
Industrial imaging, secure solutions

## Slide 5: Disadvantages
Slower than Application Specific Integrated Circuits (ASIC)
High power consumption
Not good for high quantity production
Requires knowledge of hardware design languages
Notes: Slower and require more power than ASICs
Requires knowledge of hardware design languages – more complex than C, etc.
Drawbacks or disadvantages of FPGA
Following are the disadvantages of FPGA: ➨The programming of FPGA requires knowledge of VHDL/Verilog programming languages as well as digital system fundamentals. The programming is not as simple as C programming used in processor based hardware. Moreover engineers need to learn use of simulation tools. ➨The power consumption is more and programmers do not have any control on power optimization in FPGA. No such issues in ASIC. ➨Once any particular FPGA is selected and used in the design, programmers need to make use of resources available on the FPGA IC. This will limit the design size and features. TO avoid such situation, appropriate FPGA need to be chosen at the beginning itself. ➨FPGAs are better for prototyping and low quantity production. When the quantity of FPGAs to be manufactured increases, cost per product also increases. This is not the case with ASIC implementation.

## Slide 6: Advantages
Significantly faster than microprocessors due to their parallel nature
Malicious modifications during fabrication is a lower risk
Ability to re-program
Shorter time to market
Lower non-recurring engineering costs
Notes: ability to re-program in the field to fix bugs, and may include a shorter time to market and lower non-recurring engineering costs.
Integrated circuit development costs are rising aggressively
ASIC complexity has lengthened development time
R&D resources and headcount are decreasing
Revenue losses for slow time-to-market are increasing
Financial constraints in a poor economy are driving low-cost technologies
Following are the benefits or advantages of FPGA: ➨FPGAs can be programmed at logic level. Hence it can implement faster and parallel processing of signals. This is difficult to be executed by processor. ➨Unlike ASIC which are fixed once programmed, FPGAs are programmable at software level at any time. Hence FPGA IC can be re-programmed or reused any number of times. FPGA can also be programmed from remote locations. ➨FPGA ICs are readily available which can be programmed using HDL code in no time. Hence the solution is available faster to the market. ➨Unlike ASIC which requires huge NRE (Non Recurring Expenses) and costly tools, FPGA development is cheaper due to less costly tools and no NRE. ➨In FPGA design, software takes care of routing, placement and timing. This makes lesser manual intervention. The design flow eliminates complex and time consuming place and router, floor planning and timing analysis.